## Slide 1
Arseniy Obolenskiy, Anton Gorshkov
anton.v.gorshkov@gmail.com
Ascend Hardware and Ascend C Language Introduction
Programming for AI-accelerators
Lobachevsky State University of Nizhny Novgorod
Institute of Information Technology, Mathematics and Mechanics

## Slide 2: Contents
Ascend HW Architecture
Ascend C Language Introduction

## Slide 3: Ascend HARDWARE ARCHITECTURE

## Slide 4: Ascend Hardware: Overview
Da Vinci architecture
Each DaVinci Max AI Core features a 3D Cube Tensor Computing Engine (4096 FP16 MACs + 8192 INT8 MACs), Vector unit (2048bit INT8/FP16/FP32) and scalar unit. It includes a new AI framework called "MindSpore", a platform-as-a-service product called ModelArts, and a lower-level library called Compute Architecture for Neural Networks (CANN).
Ascend 310
The Ascend 310 is an AI inference SoC, it was codenamed Ascend-Mini. The Ascend 310 is capable of 16 TOPS@INT8 and 8 TOPS@FP16. The Ascend 310 features:
2x DaVinci Max AI cores
8x ARM Cortex-A55 CPU cores
8 MB on-chip buffer
16 channel video decode – H.264/H.265
1 channel video encode – H.264/H.265
TSMC 12 nm FFC process
8 W
Ascend 910
The Ascend 910 is an AI training SoC, it was codenamed Ascend-Max, which delivers 256 TFLOPS@FP16 and 512 TOPS@INT8. The Ascend 910 features:
32x Da Vinci Max AI cores arranged in 4 clusters
1024-bit NoC Mesh @ 2 GHz, with 128 GB/s bandwidth Read/Write per core
3x 240 Gbit/s HCCS ports for Numa connections
2x 100 Gbit/s RoCE interfaces for networking
4x HBM2E, 1.2 TB/s bandwidth
3D-SRAM stacked below AI SoC die
1228 mm2 Total die size (456 mm2 Virtuvian AI SoC, 168 mm2 Nimbus V3 IO Die, 4x96 mm2 HBM2E, 2x110 mm2 Dummy Die)
32 MB on-chip buffer
128 channel video decode – H.264/H.265
TSMC 7+ nm EUV (N7+) process
350 W
The Ascend 910 Cluster has 1024–2048 Ascend 910 chips to reach 256–512 petaFLOPS@FP16. The Ascend 910 and Ascend Cluster will be available in Q2 2019.

## Slide 5: SIMT vs SIMD
SIMT
SIMD
Huawei Ascend
NVIDIA GPU
AMD GPU
Intel CPU (SSE, AVX, …)
Intel ARC GPU

## Slide 6: Ascend 910 Architecture Overview

## Slide 7: Ascend 910B Architecture Overview

## Slide 8: AICORE Level Parallelism
Parallelism is reached through:
  SIMD vectors
    Comparable with threads in NVIDIA CUDA
    blockDim
  AICORE level parallelism
    Comparable with blocks in NVIDIA CUDA
    gridDim
Huawei Ascend
NVIDIA GPU

## Slide 9: Debugging Capabilities
Ascend C can be compiled to:
  NPU binary
    Simulator and real device
  x86/aarch64 CPU
Debugging can be done using different tools in each case:
  CPU
    gdb, npuchk, cceprint, …
  Simulator
    camodel (cycle accurate simulation) logs
  Real device
    msnpureport

## Slide 10: Ascend Programming Challenges
Sophisticated HW architecture: many programmable pipes, buffers, caches
Need for explicit data transfers and manual memory management
CUBE and VECTOR unit communications are organized through external memory, it impacts mixed kernels implementation
CUBE pipeline
VEC pipeline

## Slide 11: Ascend HW: Usage Scenarios
Training
Inference
The Atlas 200 AI accelerator module (model: 3000) integrates the Ascend processor to implement image recognition and image classification on the device side. Atlas 200 is widely used in AI scenarios such as intelligent cameras, robots, and drones.
The Atlas 900 AI cluster consists of thousands of Ascend processors.
Product Line: https://e.huawei.com/en/products/computing/ascend

## Slide 12: Products That Support Ascend
Huawei CANN https://www.hiascend.com/en/software/cann
MindSpore https://gitee.com/mindspore/mindspore
OpenCV https://github.com/opencv/opencv/wiki/Huawei-CANN-Backend
OpenMMLab Detection Toolbox and Benchmark https://github.com/open-mmlab/mmdetection

## Slide 13: Programmability: Kernel (Operator) Level
Which programming interfaces are available for kernel developers?
TBE DSL
  Python API that exposes domain-specific language (DSL) for simple programming
  Easier to use but may be slow
  Currently deprecated
TBE TIK
  Python API that is suitable for low-level development with some enhancements
  Currently deprecated
CCE-C
  Suitable for low-level programming, intrinsic-based
  Poorly documented
  Not supposed to be used by end users
Ascend C Language
  Suggested for using by Huawei

## Slide 14: Programmability: Network Level
CANN stack supports integration to the following ML/DL frameworks
PyTorch kernels integration
  https://gitee.com/ascend/torch
ONNX
  https://github.com/microsoft/onnxruntime/tree/main/onnxruntime/core/providers/cann
MindSpore
  https://gitee.com/mindspore/mindspore

## Slide 15: Ascend C language

## Slide 16: Ascend C: Documentation
Website: https://www.hiascend.com/ascend-c (中文)
Detailed Programming Guide: https://www.hiascend.com/document/detail/zh/CANNCommunityEdition/80RC1alpha001/devguide/opdevg/ascendcopdevg/atlas_ascendc_10_0001.html (中文)

## Slide 17: Host and device code
Host code and device code
  Host code: code that runs on the CPU. It typically includes setup, data preparation, launching GPU/NPU kernels, and handling the results returned from the GPU/NPU.
  Device code: This is the code that runs on the GPU/NPU. Device code operates on data stored in device memory and is executed by many threads in parallel.
Host/device code split implementation in Ascend C
  Similarities with CUDA
    NPU kernel invocation logic is the same
  Difference
    API for NPU invocations has differences with CUDA one
    In addition, there is a separate CPU debug mode that allowas to execute code on CPU instead of NPU that uses differerent code invocation API
int main()
{
...
// Kernel invocation with N threads
VecAdd<<<1, N>>>(A, B, C);
...
}

## Slide 18: Ascend C By Example: HelloWorld
Example that prints “Hello World”
main.cpp
hello_world.cpp
Source code: https://gitee.com/ascend/samples/tree/master/operator/HelloWorldSample
ACL* Runtime (RT) API header file
ACL context initialization
* ACL – Ascend Compute Library
Ascend device selection
Kernel invocation
ACL context de-initialization (finalization)
Device side operator library (Ascend C API)
Device side printf-like function

## Slide 19: Ascend C By Example: build & run
CMakeLists.txt
  https://gitee.com/ascend/samples/blob/master/operator/ascendc/0_introduction/3_add_kernellaunch/AddKernelInvocationNeo/CMakeLists.txt
Build & run
rm -rf build
mkdir build
cmake -B build
cmake --build build -j
cmake --install build
./build/main
Select Ascend device chip version
Set path to Huawei CANN software stack installation
Choose execution mode:
- Hardware
- Simulator
- CPU debug
Reuse pre-defined templates for kernel development supplied with CANN stack
Create kernels library
Provide compiler options for kernels library
Build host side executable that invokes kernels from operators library

## Slide 20: Ascend C By Example: Vector Add
Device code:
  https://gitee.com/ascend/samples/blob/master/operator/ascendc/0_introduction/3_add_kernellaunch/AddKernelInvocationNeo/add_custom.cpp
Host code:
  https://gitee.com/ascend/samples/blob/master/operator/ascendc/0_introduction/3_add_kernellaunch/AddKernelInvocationNeo/main.cpp
Kernel function attribute : __global__
Device function attribute: __aicore__
Macro that is defined for CPU run: __CCE_KT_TEST__
Kernel invocation on the host code: <<< >>>

## Slide 21: Ascend C By Example: Vector Add (Pipeline Paradigm)
Device execution pipeline is split into 3 steps:
  CopyIn, Compute, CopyOut

## Slide 22: Running Ascend C Kernels
Instructions:
  https://gitee.com/ascend/samples/tree/master/operator/ascendc/0_introduction/3_add_kernellaunch/AddKernelInvocationNeo
Covered and available run scenarios:
  CPU
  NPU simulator
  NPU on-board
Dependences:
  CANN
    EE: https://support.huawei.com/enterprise/en/ascend-computing/cann-pid-251168373/software/
    CE: https://www.hiascend.com/zh/developer/download/community/result?module=cann

## Slide 23: Running Ascend C Kernels: Step-by-Step Guide

## Slide 24: Next Time
Ascend C Programming Details
Matrix Multiplication Kernel
Mixed Kernels

## Slide 25: References
Ascend C: https://www.hiascend.com/ascend-c
Ascend C Samples: https://gitee.com/ascend/samples/
Ascend C Programming Guide: https://www.hiascend.com/document/detail/zh/CANNCommunityEdition/80RC1alpha001/devguide/opdevg/ascendcopdevg/atlas_ascendc_10_0001.html
Huawei CANN Community Edition: https://www.hiascend.com/zh/developer/download/community/result?module=cann
Ascend Computing: https://e.huawei.com/en/products/computing/ascend/
TBE DSL: https://www.hiascend.com/document/detail/en/CANNCommunityEdition/600alphaX/opdevg/opdevg/atlaste_07_0001.html
TBE TIK: https://www.hiascend.com/document/detail/en/CANNCommunityEdition/600alphaX/opdevg/opdevg/atlastikapi_07_0001.html

## Slide 26: Team
Anton Gorshkov, Ph.D., Associate Professor at Lobachevsky State University, Principal Engineer at Huawei
Arseniy Obolenskiy, Senior Engineer at Huawei
Mikhail Lychkov, Senior Engineer at Huawei
Oleg Maslov, Ph.D., Expert at Huawei